## Slide 1
通信感知自适应权重
用于分布式 GA-LMB / KLA 融合
当前主线不是重做滤波器，而是在 unknown cross-correlation 下重做融合权重分配：让权重同时感知后验质量、实际链路质量和存在性决断度。
GA-LMB
distributed KLA
consensus-oriented
8-sensor distributed fusion
headline evidence
31.98%
consensus OSPA 下降
34.57%
consensus RMSE 下降
91.46%
cardinality disagreement 下降
20 paired trials, seeds 2-21
main tiered heterogeneous packet-loss scenario
Source: docs/paper/README.md; RUN/GA/GA_TIERED_LINK_ABLATION_N20_SEED1_20260512_155714.md
01

## Slide 2
POSITIONING
论文边界要先收紧：贡献是自适应融合权重，而不是新滤波器家族
这会让方法、实验和结论都围绕 distributed KLA-based LMB fusion 的同一个成功标准展开。
问题设定
通信受限的分布式 GA-LMB / KLA 融合
unknown cross-correlation 下 KLA 仍是合理基线；真正脆弱的是固定或纯拓扑权重。
方法焦点
三因子权重 backbone + 分支化 refinement
covariance、realized link quality、existence confidence 是主干；FID-FIA 只进 existence 分支。
成功标准
优先改善跨节点 consensus
consensus OSPA/RMSE/cardinality 是 primary；local tracking 作为 safeguard，防止一致到错误答案。
不要把正文写散：history / freshness / association ambiguity / NIS 只能作为 secondary 或 appendix evidence。
主 claim 必须能回到：adaptive weight allocation under communication constraints。
Source: docs/paper/00_positioning.md; docs/paper_line/PAPER_MAIN_NARRATIVE_LOGIC_CN.md
02

## Slide 3
SCENARIO
主场景保留原 4+4 编队，但用异构通信把固定权重的弱点放大
evaluation frame
8
mobile sensors, two 4-sensor formations
10
targets in 3 + 3 + 4 staggered births
100
simulation steps; MC means reported
tiered packet loss: [0, 0.1, 0.2, 0.5]
level counts: [1, 4, 1, 2]
mean pDrop preserved at 0.2
通信图：formation 内部强连接，跨 formation 一对一连接。
固定基线：local neighborhood 内 Metropolis weights；main paper evidence 以 tiered-drop GA 为主。
Source: docs/paper/06_experimental_setup.md; docs/paper/figures/figure_simulation_scenario.pdf
03

## Slide 4
PIPELINE
方法嵌入现有分布式 GA-LMB 流水线，只改变邻域融合权重
1
local measurement update
各节点先得到自己的 LMB posterior
2
neighborhood communication
带 bandwidth / packet loss 的消息交换
3
adaptive fusion weights
按 posterior quality + link + existence 重分配权重
4
branch-decoupled KLA
spatial 与 existence 分支分别融合
因此 slide 里的技术说法应保持克制：这是 conservative KLA fusion 的权重分配改进，而不是替换 LMB/GA/KLA 框架。
Source: docs/paper/05_method_adaptive_kla.md; docs/paper/els-cas-templates/figs/paper-figure1-crop.png
04

## Slide 5
METHOD
三因子 backbone 是主干；branch decoupling 和 FID-FIA 是分支化 refinement
shared backbone
mask x covariance x link quality x existence confidence
spatial branch
cov/link + weak structure prior, keep RMSE-oriented path
existence branch
existence confidence + FID-FIA cue, target cardinality agreement
NIS / history / freshness: optional, not headline
讲法重点：不是“模块越多越好”，而是把能被证据支持的信号放进对应分支。
Source: docs/paper/05_method_adaptive_kla.md; docs/paper/els-cas-templates/figs/paper-figure2-crop.png
05

## Slide 6
EXISTENCE CONFIDENCE
existence confidence 补上 covariance 和 link quality 看不到的一维
Bernoulli decisiveness
c = |2r - 1|
r 接近 0 或 1 时更果断；r 接近 0.5 时更模糊。
covariance: 只看空间集中度，不表达目标是否存在。
link quality: 只看信息是否送达，不表达 posterior content 是否可信。
existence confidence: 给 cardinality / existence 分支一个直接信号。
这也是为什么最终方法不把 FID-FIA 作为 whole-posterior scalar weight，而是只把它作为 existence/cardinality cue。
Source: docs/paper/05_method_adaptive_kla.md; docs/paper/figures/figure3_existence_confidence_curve.png
06

## Slide 7
EVIDENCE STACK
证据要分层：主线讲最强结果，弱模块留作 appendix 解释取舍
PRIMARY
tiered packet-loss main result
20 paired trials: fixed / FID-FIA / backbone / proposed
DIAGNOSTIC
factor ablation
fixed -> cov -> link -> exist -> decoupled -> FID-FIA existence
SUPPORT
ideal communication + AA
回答是否只是补救丢包；AA 只作外推迹象
APPENDIX
NIS / history / freshness
记录探索过的方向，但当前证据弱、混合或负向
deck rule
1
每页一个 claim
1
一个 proof object
0
不讲未被证据支持的创新
这样排布能解释为什么 main paper 不把 NIS/history/freshness 写成贡献，同时也不浪费已有负结果材料。
Source: docs/paper/09_figures_tables_and_gaps.md; docs/paper/Appendix_B_additional_attempts.md
07

## Slide 8
MAIN RESULT
tiered-drop 20-trial 主结果：proposed arm 在三项 consensus 指标上全优
OSPA
fixed
2.454
FID-FIA
1.820
backbone
1.786
proposed
1.669
RMSE
fixed
2.336
FID-FIA
1.647
backbone
1.563
proposed
1.528
CARD
fixed
0.715
FID-FIA
0.126
backbone
0.193
proposed
0.061
time-series proof: adaptive method 在主要轨迹上持续低于 fixed baseline
31.98%
OSPA reduction vs fixed
34.57%
RMSE reduction vs fixed
91.46%
cardinality reduction vs fixed
解释口径：FID-FIA baseline 已经是强 cardinality baseline；新的 branch-decoupled fusion 同时超过它和旧 backbone。
Source: RUN/GA/GA_TIERED_LINK_ABLATION_N20_SEED1_20260512_155714.md; docs/paper/figures/figure4_main_ga_consensus.pdf
08

## Slide 9
SAFEGUARD
local metrics 说明：一致性提升不是靠错误局部目标数换来的
Arm
E-OSPA
RMSE
CardErr
fixed weights
2.853
1.638
1.455
Scalar FID-FIA
2.183
1.716
0.392
branch-decoupled backbone
2.329
1.599
0.579
proposed refinement
2.009
1.705
0.222
safeguard verdict
best local E-OSPA
best local CardErr
local RMSE 不如旧 backbone，但仍略优于 scalar FID-FIA baseline。
fixed CardErr
1.455
FID-FIA CardErr
0.392
backbone CardErr
0.579
proposed CardErr
0.222
讲法
最终方法的 cardinality consensus 优势，同时体现在 truth-referenced local CardErr 上；这比只展示 consensus 更容易 defend。
因此结论应写成“consensus-first with local safeguards”，不要写成所有 local metric 无条件全面提升。
Source: RUN/GA/GA_TIERED_LINK_ABLATION_N20_SEED1_20260512_155714.md
09

## Slide 10
ABLATION
消融表明：link quality 是最大通信增益，FID-FIA existence cue 给最终跨越
fixed
2.448
OSPA
0.679
CARD
cov
2.082
OSPA
0.458
CARD
+link
1.830
OSPA
0.231
CARD
+exist
1.830
OSPA
0.231
CARD
decoupled
1.821
OSPA
0.232
CARD
proposed
1.669
OSPA
0.061
CARD
读法
covariance 必要但不充分；link quality 带来最大通信增益；20-trial 下 existence confidence 的结论要收窄；最终 FID-FIA existence 分支给 cardinality 跨越。
Source: RUN/GA/GA_TIERED_LINK_ABLATION_MAIN20_20260507.md; docs/paper/els-cas-templates/sections/06_results.tex
10

## Slide 11
SUPPORTING EVIDENCE
理想通信下仍有效：方法不是只在补救 packet loss
Arm
OSPA
RMSE
Card
Ordinary GA
1.704
1.532
0.162
Branch backbone
1.482
1.238
0.132
Scalar FID-FIA
1.532
1.332
0.054
Proposed
1.433
1.309
0.050
15.9%
ideal OSPA reduction vs ordinary GA
69.1%
ideal cardinality reduction
10.6%
local E-OSPA reduction
AA secondary generalization
consensus OSPA 4.349 -> 3.811
consensus RMSE 19.098 -> 16.472
cardinality 0.421 -> 0.307
讲法：ideal communication 支撑“更合理的 distributed fusion weighting rule”；AA 只作为外推迹象，不与 GA/KLA 主线并列。
Source: RUN/GA/GA_IDEAL_COMM_MAIN20_PAIRED_20260507.md; RUN/GA/GA_TIERED_LINK_ABLATION_N20_SEED1_20260513_014211.md
11

## Slide 12
CLOSE
最终可讲的故事：通信约束下，权重分配才是分布式 KLA 的关键杠杆
keep in main story
fixed KLA weights are brittle under heterogeneous communication
covariance + realized link quality + existence confidence is the backbone
branch decoupling preserves the spatial path while existence-FID-FIA supplies cardinality gain
consensus metrics are primary; local metrics are safeguards
move to appendix or future work
NIS: plain harmful; robust not better than no-NIS in latest table
history / freshness: mixed or effectively flat
association ambiguity / cardinality consensus: pilot-level or negative
state-dependent quality + false tracks: useful next scenario, framed as baseline plus perturbations
下一步最值得补的不是新模块，而是把 final method 的 paired baseline reuse 和更大 Monte Carlo 统计补齐，再把 4+4 新扰动场景作为 robustness extension。
Source: docs/paper/README.md; docs/paper/Appendix_B_additional_attempts.md; memory-backed 4+4 framing
12